## Slide 1: IANA Code Point Assignment for New BMP Statistics Types
Mukul Srivastava (Juniper Networks)
Yisong Liu (China Mobile)
Changwang Lin (New H3C Technologies)
Jinming Li (China Mobile)
draft-ietf-grow-bmp-bgp-rib-stats-05

## Slide 2
Overview
Stats Reports messages: Be used by the monitoring station to observe interesting events that occur on the router
New BMP Statistics Types: Define some statistics types to update RFC 7854 for enriching events of interest to routers
  More detailed counting types for inbound and outbound routing policies
  RPKI verification result
  IETF-118 IETF-119 IETF-120

## Slide 3
Updates of version 05
Completed IANA code points assignment application.
Stat Type | Description | Reference
18 | (64-bit Gauge) Number of routes currently in Adj-RIBs-In Pre-Policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
19 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-In Pre-Policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
20 | (64-bit Gauge) Number of routes currently in Adj-RIBs-In Post-Policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
21 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-In Post-Policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
22 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI rejected by inbound policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
23 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI accepted by inbound policy (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
24 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI selected as primary route. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
25 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI selected as backup route. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
26 | (64-bit Gauge) Number of routes in per-AFI/SAFI suppressed by configured route damping policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
27 | (64-bit Gauge) Number of routes in per-AFI/SAFI marked as stale by any configuration. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]

## Slide 4
Updates of version 05
Stat Type | Description | Reference
28 | (64-bit Gauge) Number of routes in per-AFI/SAFI marked as stale by LLGR. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
29 | (64-bit Gauge) Number of routes left until reaching the received route threshold. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
30 | (64-bit Gauge) Number of routes in per-AFI/SAFI left until reaching the received route threshold. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
31 | (64-bit Gauge) Number of routes left until reaching the license-customized route threshold. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
32 | (64-bit Gauge) Number of routes in per-AFI/SAFI left until reaching the license-customized route threshold. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
33 | (64-bit Gauge) Number of routes currently rejected due to exceeding the length threshold of as-path. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
34 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI rejected due to exceeding the length threshold of as-path. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
35 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-In Post-Policy invalidated after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
36 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-In Post-Policy validated after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
37 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-In Post-Policy not found after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
38 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI rejected by outbound policy. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]

## Slide 5: https://www.iana.org/assignments/bmp-parameters/bmp-parameters.xhtml
Updates of version 05
Stat Type | Description | Reference
39 | (64-bit Gauge) Number of routes currently refused by exceeding the length threshold of as-path. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
40 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI refused by exceeding the length threshold of as-path. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
41 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-Out Post-Policy invalidated after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
42 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-Out Post-Policy validated after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
43 | (64-bit Gauge) Number of routes currently in per-AFI/SAFI Adj-RIBs-Out Post-Policy not found after verifying route origin AS number through the ROA of RPKI. (TEMPORARY - registered 2024-10-18, expires 2025-10-18) | [draft-ietf-grow-bmp-bgp-rib-stats-04]
44-65530 | Unassigned | 

## Slide 6
Next Steps
Seeking more feedback from WG
Planning for last call
Any comments?